## Slide 1: Digital Signal Processor Chip Design
TEAM ADD
Cary Converse
Mark Galligan
Belinda Stuart
Chenqian Gan
Portable Instruments Company (PICo)
Contract Proposal

## Slide 2: Project Description
DSP Block Design Specification
ALU Functions
NOP
Pass A
Add/Sub
Shift
And
OR
Counter

## Slide 3: Overview
Sizing/ Buffering/Registers
Adder/Subtractor
“8:1” MUX
Counter
Muxed Shifter
Design Benefits and Trade-offs
Metric Evaluation

## Slide 4: Sizing/Buffering/Registers
Sizing
  Almost all parts minimum sized
    Basic function input caps within fan-out of 4
    AND, OR, NOP, PASS A
Buffering
  Large buffers on A and B register outputs before gate inputs
  Buffers usually outside of gates
Registers
  Reduce clock skew
    Buffer for clock to match with not-clock signal

## Slide 5: ADDER/SUBTRACTOR
Overview
  Single Adder/Subtractor block
    Mirror Adder : 2-bit
      Cascaded Component
      Takes advantage of inversion
      Cuts down ripple of carry
  Control bit selects ADD or SUB
    Defined by OP Code
    Sub Control = 1
      Also used in 2’s complement adder carry

## Slide 6: “8:1” MUX (7:1 MUX)
Combination of 6:1 and 2:1 MUXes
  6:1 MUX for other functions
    Output of 6:1 MUX as input to 2:1 MUX
  Final 2:1 MUX for outputs
MUXed to minimize delay
  ADD/SUB is the critical path
    Separate 2:1 MUX for speed
  2:1 MUX output Preselected

## Slide 7: Arbitrary Function: Counter
Functionality
  Count = [(S0 (+) heldS0) + (S1 (+) heldS1) + (S2 (+) heldS2) ]’
    0th -> always invert
  Clear =[ (S0 (+)1) + (S1 (+) 1) + (S2 (+) 1) ]’
    Counter opcode is 111
  Determines the number of times a specific function is called
    Function opcode specified by 3 least significant bits of input A
  Iterates until called again to output the count value
Usage
  Self-diagnostics
    user input, conditional statements, self-modifying code, large / inaccessible source code, etc.

## Slide 8: Counter Schematics
1 Bit Counter
Hold Control Bit

## Slide 9: Shifter
Design specified a small number of bit shifts
  Practical to implement using MUXes
  More complexity (e.g. a barrel or logarithmic shifter) is not needed

## Slide 10: Design Benefits and Trade-offs
Benefits
Easy to implement
  Standard library
  Bit-sliced design for bit-width flexibility
Size Savings
  Minimized functions off critical path
  Re-use hardware (ADD/SUB)
Lower power consumption
  Compared to previous year projects
Trade-offs
Large MUX size
  Use of NAND gates for simplicity
  Wary about driving transmission gates
Large Adder Sizing
  Better fan-out
  Easy to cascade
  Reduced carry delay

## Slide 11: Metric Values – Team ADD 2009
Measurement | Value
“Area” | 0.0222 m
Avg. Energy per Cycle | 2.24134*10-9J
Delay | 9.446*10-9s
Final Metric | 4.439730*10-27 mJs2

## Slide 12: Team ADD: Size Breakdown
ALU Function | Size (um)
Pass A | 384
AND | 264
OR | 312
ADD/SUB | 5928
Shifter | 807
Counter | 3705
MUX | 6192
Chip Component | Size (um)
Registers and Buffer Size | 4608
Total ALU Size | 17592
Total Size | 22200

## Slide 13: Average Energy and Delay
Avg. Energy Formula
  VDD = 5V  Avg. Energy = 2.24134*10-9J
    Alternate calculation: VDD = 2.5V; Avg. Energy = 2.73063*10-10 J
  Final Value: 2.24134*10-9J
Delay
  Critical Path: path through Subtractor
  Final Value: 9.446*10-9s

## Slide 14: 2008 Metric Values
Team | Equivalent 2010 Metric Value (m*s^2*J) | Delay (s) | "Area" (m) | Power (W) | Calculated Energy per Cycle (J)
Converse, Galligan, Stuart, Gan | 4.439730*10-27 | 9.446*10-9 | 2.22*10-2 | 2.1095*10-2 | 2.24134*10-9
Andrews, Mapar, Stefanelli | 2.245E-27 | 1.000E-08 | 7.128E-03 | 3.150E-02 | 3.150E-09
D. Chen, J. Chen, Headley, Willstatter | 2.742E-26 | 1.150E-08 | 1.695E-02 | 1.223E-01 | 1.223E-08
Ashworth, Healy, Williams | 6.531E-27 | 6.000E-09 | 1.278E-02 | 1.420E-01 | 1.420E-08
Benson, Combs, Lumsden | 2.614E-27 | 9.670E-09 | 1.165E-02 | 2.399E-02 | 2.399E-09

## Slide 15: Questions?